## Slide 1: DirectTranscription.jl : A Julian Approach to Multi-Phase Trajectory Optimization
Grant R. Hecht

## Slide 2: Overview
Introduction and motivation
Optimal control and nonlinear programming
Direct transcription with Lobatto IIIA Collocation
Overview of DirectTranscription.jl design
A simple example : The Brachistochrone
Conclusion

## Slide 3: Why another trajectory optimization tool?
Existing multi-phase trajectory optimization tools
  GPOPS-II → Requires license and written in pure MATLAB
  Dymos → User provided functions written in Python
  CSALT → No AD and poor documentation, requires SNOPT
None of these tools are extensible!
  You’re stuck with the transcription methods you’re given
  Limits research on new transcription methods
  Many specialized tools developed from scratch

## Slide 4: Goals of DirectTranscription.jl
Use not limited by paywall
Fast performance
  This is HPC II after all…
Fast user development
Options for computing Jacobians of user functions
  Source-to-source, forward, and reverse mode AD
  User provided analytical Jacobians
  Finite difference
Extensible

## Slide 5: Why Julia?
High-level dynamic language with JIT compilation
  Syntax similar to MATLAB and Python
  Speed that nearly rivals C/Fortran
Multiple dispatch paradigm
  Extensibility of nearly all Julia packages
Many differentiation libraries
  Zygote.jl and Enzyme.jl (Source-to-source AD)
  ForwardDiff.jl and ReverseDiff.jl (Forward and reverse mode AD)
  FiniteDiff.jl (Sparse Jacobians via coloring vectors)

## Slide 6: Sparse Nonlinear Programming
Minimize: | 
Subject to: | 
Minimize: | 
Subject to: | 
is a vector of decision variables,
is a nonlinear function to be minimized subject to constraints
is a vector of nonlinear functions,
  In general, are very sparse
Can exploit separability [2]:
NOTE: Only need to differentiate

## Slide 7: The multi-phase optimal control problem
Optimal control problem = NLP problem with infinite number of variables [1]
The optimal control problem with phases:
Minimize: | 
Subject to: | 
Minimize: | 
Subject to: | 

## Slide 8: Lobatto IIIA Collocation
Method to “transcribe” the optimal control problem as an NLP problem
Class of implicit Runge-Kutta methods
Lobatto IIIA S = 3 defect constraints [2]:
where:

## Slide 9: DirectTranscription.jl Design

## Slide 10: High Level Overview
Trajectory “struct” is the highest-level data structure
  Contains NLP solver wrapper
  Set of point functions and phases
Phase is abstract type with subtypes which apply various transcriptions
  Subtypes of Phase must define
    EvaluateFunctions,EvaluateJacobians,GetNLPMatricies, etc
  Users can implement their own subtypes of Phase
    Allows for quick implementation of new transcriptions
UserFunction is abstract type with subtypes to wrap various user funcs.
  ADPointFunction, AnalyticPathFunction, etc… wrap user functions and evaluate Jacobians with their unique method(s)

## Slide 11: The Phase Abstract Type
Easily extendable for implementation of new transcriptions
  Contains decision vector specific to the phase
  Must fill and provide phase NLP sub-problem in the form:
  Must define specific functions
    EvaluateFunctions – Fills the vector
    EvaluateJacobians – Fills Jacobian of ,
    GetNLPMatricies – Provides to Trajectory

## Slide 12: The UserFunction Abstract Type
Subtypes of UserFunction wrap user provided functions
  Must define EvaluateJacobian functions to evaluate the state, control, static parameter, and time Jacobians
  Must define GetSparsityPattern functions to provide sparsity of each Jacobian
  Can be extended to employ any Jacobian evaluation method user needs

## Slide 13: DEMO: The Brachistochrone

## Slide 14: Summary
Can use Ipopt (free) or Snopt (paid)
Already quite fast but much room for performance optimizations
  Better management of sparse matrices
  Parallel evaluation of user functions and Jacobians
Clean user interface
Written with extensibility in mind
  User defined domain specific transcriptions
  User defined UserFunction’s
    Jacobian evaluation methods not implemented in package
    Non-standard user function form

## Slide 15: References
[1] Betts, J.T. Practical Methods for Optimal Control and Estimation using Nonlinear Programming, 2nd edn. Society for Industrial and Applied Mathematics, Philadelphia (2010)
[2] Betts, J.T. Using Direct Transcription to Compute Optimal Low Thrust Transfers Between Libration Point Orbits. In: Fasano, G., Pintér, J.D. (eds) Space Engineering. Springer Optimization and Its Applications, vol 114. Springer, Cham. (2016) https://doi.org/10.1007/978-3-319-41508-6_2